Discover UEFI
with U-Boot
2020-02-01, Heinrich Schuchardt
CC-BY-SA-4.0

---
About Me
- Software-Consultant ERP, Supply Chain
- Contributor to U-Boot since 2017
- Maintainer of the UEFI sub-system
  since 02/2019

---
I Want a Network Drive
- Many single board computers have neither SATA nor PCIe.
- For many boards Ethernet is the fastest connector.
- An SSD drive costs more than most SBCs.

---
Network Booting in U-Boot
- BOOTP server provides tFTP server address and name of boot script
- Boot script loads kernel via tFTP or NFSv3 (UDP)
- No authentication at all
BOOTP
tFTP
NFSv3

---
iSCSI
- SCSI protocol transported via TCP
- Offers entire data stores (LUNs) to iSCSI client
- Mutual authentication of client and server
  with CHAP: MD5(ID + secret + challenge)
- Further security via VLAN separation and IPsec

---
iPXE
Swiss army knife of network booting:
- Boot from HTTP(s) server
- Boot via iSCSI
- Boot via FcoE
  (Fibre Channel over Ethernet)
- Boot via AoE (ATA over Ethernet)
- Scriptable
- Can be built as UEFI payload
See https://ipxe.org,
Developer Michael Brown <mcb30@ipxe.org>

---
UEFI in U-Boot Started 2016

---
First Try
-2147483639 = 0x80000009 = EFI_OUT_OF_RESOURCES

---
My U-Boot Journey Begins
Bare Minimum
to start GRUB
iSCSI boot
with iPXE
Run EFI Shell
and EDK II SCT
2016/17
2018
2019
together with 40 UEFI sub-system contributors

---
 Where Sits UEFI?
Booting with ATF on ARMv8
Operating System
BSD, Linux, Windows
Trusted Apps
Boot Loader
GRUB, iPXE
BL31
EL3 Runtime
BL32
Secure EL1 Firmware
BL33
U-Boot, EDK2, ...
PSCI
OP-TEE OS
BL2
Trusted Boot Firmware
BL1
Boot ROM
ATF – ARM Trusted Firmware
OP-TEE – Open Portable Trusted Execution Environment
PSCI – Power State Coordination Interface
UEFI – Unified Extensible Firmware Interface
UEFI

---
UEFI
Protocols
Boot Services
Run Time Services
Events, timers, task priority
Variable services
Device path
Memory allocation
Time services
Driver model
Protocol handling
Virtual memory services
Console support
Miscellaneous
Media access
Image services
Miscellaneous
Network protocols
Configuration Tables
ACPI
SMBIOS
Device Tree
System Table

---
“Atoms” of UEFI
- Handles
  - void* pointer
  - Protocols are installed
    on handles
- Events
  - Triggered by timer or service call
  - Callback function

---
Lifetime of a Handle
Creation by
installing first protocol
Deletion by
removing last protocol
InstallProtocolInterface
InstallMultipleProtocolInterfaces
UninstallProtocolInterface
UninstallMultipleProtocolInterfaces

---
Driver
- Handle with EFI_DRIVER_BINDING_PROTOCOL
  - GUID
    {0x18A031AB, 0xB443, 0x4D1A, {0xA5, 0xC0, 0x0C, 0x09, 0x26, 0x1E, 0x9F, 0x71}}
  - Protocol Interface Structure
    - Supported()
    - Start()
    - Stop()
    - Version
    - ImageHandle
    - DriverBindingHandle

---
Device (aka Controller)
- Handle with the EFI_DEVICE_PATH_PROTOCOL
  - Sequence of device path nodes
  - Arranges devices in a tree
PciRoot(0x0)
PciRoot(0x0)/Pci(0x1,0x1)
PciRoot(0x0)/Pci(0x1,0x1)/Pci(0x0,0x0)/NVMe(0x1,AD-A9-B1-73-55-38-24-00)
PciRoot(0x0)/Pci(0x1,0x1)/Pci(0x0,0x0)/NVMe(0x1,AD-A9-B1-73-55-38-24-00)
/HD(1,GPT,F24494A4-585B-4E34-A367-4DC70CFFC93D,0x800,0x1DC800)
PciRoot(0x0)/Pci(0x8,0x2)
PciRoot(0x0)/Pci(0x8,0x2)/Pci(0x0,0x0)/Sata(0x0,0x0,0x0)
/HD(1,GPT,11C3D446-F6E4-4C67-937E-992AFC6F454F,0x800,0x108800)

---
Attaching Drivers
- ConnectController() boot service
  - calls Supported() methods of all drivers to find matches for controller
  - calls Start() method of the matching drivers
- Driver
  - installs protocols on controller
  - may create child controllers

---
U-Boot Exposes Ethernet
U-Boot’s UEFI
sub-system
U-Boot
Drivers
EFI Block Device Driver
Simple Network
Protocol
Network Driver

---
U-Boot Provides Network
- U-Boot exposes handle with
  - EFI_SIMPLE_NETWORK_PROTOCOL
    transmits layer 2 Ethernet frames
  - EFI_DEVICE_PATH_PROTOCOL
    /VenHw(U_BOOT_GUID)/MAC(e52c7d926d5c,1)

---
U-Boot EFI Block Device Driver
- U-Boot provides a driver that binds to handles exposing the the EFI_BLOCK_IO_PROTOCOL
- EFI_BLOCK_IO_PROTOCOL
  - Read from and write to block device, e.g.
    SATA, NVMe, SD-card, eMMC, USB

---
iPXE Exposes Block IO Protocol
iPXE
U-Boot’s UEFI
sub-system
U-Boot
Drivers
EFI Block Device Driver
Block IO
Protocol
iSCSI Driver
TCP/IP Driver
Simple Network
Protocol
Network Driver

---
iPXE Network Handle
- iPXE creates new handle with
  - EFI_SIMPLE_NETWORK_PROTOCOL
  - EFI_NETWORK_INTERFACE_IDENTIFIER_PROTOCOL
  - EFI_NETWORK_INTERFACE_IDENTIFIER_PROTOCOL_31
  - EFI_COMPONENT_NAME2_PROTOCOL
  - EFI_LOAD_FILE_PROTOCOL
  - EFI_DEVICE_PATH_PROTOCOL
    /VenHw(U_BOOT_GUID)/MAC(e52c7d926d5c,1)/MAC(e52c7d926d5c,1)

---
IPXE Block Device Handle
- iPXE creates new handle with
  - EFI_BLOCK_IO_PROTOCOL
  - EFI_DEVICE_PATH_PROTOCOL
    /VenHw(U_BOOT_GUID)/MAC(e52c7d926d5c,1)/MAC(e52c7d926d5c,1)
    /VenHw(IPXE_BLOCK_DEVICE_PATH_GUID,
    "iscsi:192.168.1.9:::1:iqn.2000-01.de.xypron:pine-a64-lts")

---
iPXE Connects Controller
iPXE
U-Boot’s UEFI
sub-system
U-Boot
Drivers
Block IO
Protocol
EFI Block Device Driver
iSCSI Driver
TCP/IP Driver
Simple Network
Protocol
Network Driver

---
ConnectController
- iPXE calls ConnectController() for handle with EFI_BLOCK_IO_PROTOCOL
- U-Boot identfies the driver via the supported() method of the EFI_DRIVER_BINDING_PROTOCOL
- U-Boot starts the driver

---
U-Boot Discovers Partitions
iPXE
U-Boot’s UEFI
sub-system
U-Boot
Drivers
Simple
File Protocol
FAT Driver
Block IO
Protocol
EFI Block Device Driver
iSCSI Driver
TCP/IP Driver
Simple Network
Protocol
Network Driver

---
U-Boot Block IO Driver
- Creates U-Boot block IO device
- Analyses partition table
- Creates new handles for each partition and installs
  - EFI_SIMPLE_FILE_SYSTEM_PROTOCOL
  - EFI_BLOCK_IO_PROTOCOL
  - EFI_DEVICE_PATH_PROTOCOL
    /VenHw(U_BOOT_GUID)/MAC(e52c7d926d5c,1)/MAC(e52c7d926d5c,1)
    /VenHw(IPXE_BLOCK_DEVICE_PATH_GUID,
    "iscsi:192.168.1.9:::1:iqn.2000-01.de.xypron:pine-a64-lts")
    /HD(1,MBR,0x4a8807bd,0x800,0x2f000)

---
iPXE and U-Boot Loading File
iPXE
U-Boot’s UEFI
sub-system
U-Boot
Drivers
Load File
Protocol
Simple
File Protocol
FAT Driver
Block IO
Protocol
EFI Block Device Driver
iSCSI Driver
TCP/IP Driver
Simple Network
Protocol
Network Driver

---
GRUB Loading Kernel
GRUB
iPXE
U-Boot’s UEFI
sub-system
U-Boot
Drivers
GRUB Binary
Simple
File Protocol
FAT Driver
Block IO
Protocol
EFI Block Device Driver
iSCSI Driver
TCP/IP Driver
Simple Network
Protocol
Network Driver

---
Take Away
Providing UEFI in U-Boot as a standardized API allows for easy integration with other software

---
Implementation Events
- U-Boot is single threaded
- No interrupts supporting networking, timers
Call event handling routines in
  - console routines
  - network routines
  - CheckEvent(), WaitForEvent(),
    RestoreTPL(), Stall()

---
Integration of UEFI sub-system
- U-Boot is in the middle of moving from legacy drivers to a device tree based driver model
- UEFI sub-system sits on top of U-Boot rather than being integrated into U-Boot driver model

---
Development Targets
- Support subset of UEFI specification
  - Embedded Base Boot Requirements (EBBR)
    - Boot services
    - Run time services
    - Required elements according to
      UEFI 2.8, chapter 2.6
- Stay small
  - 31000 lines, ca. 70 kiB in U-Boot binary

---
Achievements in 2019
- Missing boot services added
- Major improvements in UEFI standard compliance
  https://github.com/U-Boot-EFI/u-boot-sct-results
- U-Boot runs EFI shell on ARM, x86, x86_64
- U-Boot runs EDK II SCT on ARM, x86

---
Usage in Distributions
- Fedora, Suse use GRUB EFI by default to boot from U-Boot to Linux
- OpenBSD and FreeBSD rely on U-Boot UEFI for booting.
- The Debian installer sets up GRUB EFI if started via UEFI. Manual setup is needed to get DTB updates.

---
Fedora Wiki (2018-07-03)
- We've supported uEFI on aarch64 as the only way of booting Fedora supporting both Tianocore, proprietary uEFI implementations and since Fedora 27 we've supported uEFI via u-boot too.
- The uEFI provided by u-boot is now stable enough that we can now move ARMv7 to this method too allowing us to move ARMv7 to grub2-efi and have a single standard booth path/stack for both ARMv7 and aarch64.
https://fedoraproject.org/wiki/Changes/uEFIforARMv7

---
TODOs
- Fix remaining SCT compliance issues
- Support for variables at runtime
- Secure UEFI boot
- Integration with U-Boot’s driver model – depends on completion of U-Boot’s conversion to driver model

---
Work in Progress
- Verified UEFI Boot via FIT images
  Cristian Ciocâltea
- UEFI Secure Boot
  Takahiro Akashi (Linaro)
- EFI_RNG_PROTOCOL based on hardware RNG
  Sugosh Gani (Linaro)